ATHEνA Non-Thermal Radiation Code

Contributors (in alphabetical order)
Apostolos Mastichiadis, Maria Petropoulou

Description
Radiative transfer code for non-thermal leptonic and hadronic processes (only synchrotron for the latter) in spherical geometry.
Solves a system of coupled integro-differential equations for the energy and temporal evolution of non-thermal particle populations (protons,electrons/positrons, photons) injected in a spherical volume.

Code specifications
Written in FORTRAN 77. Uses routine D02EJF from the NAG library (https://www.nag.com/numeric/fl/nagdoc_fl24/pdf/d02/d02ejf.pdf)

Requirements
- g77 Fortran compiler
- NAG library
Some information for installation in Ubuntu based-systems follows.

 g77 Fortran compiler
for more info visit also https://askubuntu.com/questions/837618/need-the-gnu-g77-fortran-compiler-on-ubuntu-16-04-having-issues

1) update repositories... add old ones

sudo kate /etc/apt/sources.list
add the following lines:
deb http://old-releases.ubuntu. hardy universe
deb-src http://old-releases.ubuntu. hardy universe
deb http://old-releases.ubuntu. hardy-updates universe
deb-src http://old-releases.ubuntu. hardy-updates universe
sudo apt-get update
2) install the g77 compiler
sudo apt-get install g77
3) add paths in .bashrc
add following lines in .bashrc:
LIBRARY_PATH=/usr/lib/x86_64-
export LIBRARY_PATH
4) comment out old repositories
kate /etc/apt/sources.list
comment the following lines:
# deb http://old-releases.ubuntu. hardy universe
# deb-src http://old-releases.ubuntu. hardy universe
# deb http://old-releases.ubuntu. hardy-updates universe
# deb-src http://old-releases.ubuntu. hardy-updates universe
sudo apt-get update
5) create proper soft links if needed (links in /usr/lib)
sudo ln -s /usr/lib/gcc/x86_64-linux-gnu/5/libgcc_s.so /usr/lib/libgcc_s.so
6) install NAG (see below)
– Installation of NAG library*
linux> gunzip -c nag17.tar.gz | tar xvf -
linux> cd nag17
linux/nag17> cd scripts
linux/nag17/scripts> ./compile
linux/nag17/scripts>./
The last command creates the library named 'libnag.a' (inside the 'linux/nag17' directory).
You can move it to '/usr/local/lib' or '/usr/lib'. You simply call it with the flag '-lnag':
linux> g77 -o tst.x tst.f -lnag
If you put it in some other directory, e.g. 'home/harold/lib' , you have to give the full path:
linux> g77 -o tst.x tst.f -lnag -L/home/harold/lib
In 'linux/nag17/examples/" there are examples for all routines.

* Currently using NAG/F77 MARK 17 library (nag17.tar.gz) A more updated version of the library can also be downloaded. The d02ejf routine is part of the newest version (https://www.nag.com/numeric/nl/nagdoc_27/flhtml/d02/d02intro.html)

NOTE – If needed, add repository and install missing library. In the following example, the missing library during installation is libxp6:

deb http://security.ubuntu.com/ precise-security main
sudo apt update
sudo apt install libxp6

Usage
To compile type: g77 -o code.out code.f -lnag -O3 -funroll-loops
To run type: ./code

Summary of physical processes
- Protons: external injection, escape, synchrotron losses
- Electrons/positrons: external injection, escape, synchrotron losses, inverse Compton scattering losses, injection from photon-photon pair production
- Photons: escape, injection from synchrotron, injection from inverse Compton scattering, losses from photon-photon pair production, losses from synchrotron self-absorption.

Code Features
- Time-dependent calculations.
- Energy conservation.
- Linear and non-linear electromagnetic cascades.
- Option for power law (PL), broken power law (BPL), and grey-body external photon fields.
- Option for power law (PL) and broken power law (BPL) injection of electrons and protons.
- Option for sharp or super-exponential high-energy cutoff for PL and BPL injection of electrons and protons.

Description of input file

Symbol	Description	Value or Units	Comments
ireadin	Integer	0/1	Flag for running code from previous output. If ireadin=0, the code starts from the initial conditions provided in input file. If ireadin=1, the code starts from previously stored output files (dum_r4.dat). NOTE – when using ireadin=1, bfield should not be changed.
npdec	Integer	10	Not to be changed
nsteps	Integer		How often to save output files
nout	Integer		How often (in code time steps) to print output on screen
tmax	Real		Max time of physical problem
gpexmx	Real	In log10	Max bin proton Lorentz factor array. NOTE – 100 x larger than actual max proton Lorentz factor (gpexmx=2+gpextmx)
ypmin	Real	In log10	Number density (in code units) of background proton/neutron array (used in initialization of the proton/neutron array)
yemin	Real	In log10	Number density (in code units) of background electron/neutrino array (used in initialization of the electron/neutrino array)
ygmin	Real	In log10	Number density (in code units) of background photon array (used in initialization of the photon array)
tol	Real	1e-5 to 1e-4	Controls the error in the integration performed by the d02ejf routine. NOTE – to start from existing output (ireadin=1) usually tol must be reduced to 1e-5.
slpinj	Real	2. (default)	Power-law slope of proton background array
sleinj	Real	2. (default)	Power-law slope of electron background array. NOTE – can be changed if the code crashes (typical values between 2-3)
slginj	Real	2. (default)	Power-law slope of photon background array
radius	Real	In log10 [cm]	Radius of spherical region
bfield	Real	[Gauss]	Magnetic field strength
iprext	Integer	0/1	Flag for switching off/on external injection of protons with power law (PL) energy spectrum
gpextmn	Real	In log10	Min value of proton PL or BPL
gpextmx	Real	In log10	Max value of proton PL or BPL
slprints	Real		Slope of proton PL. NOTE – the code crashes if slprints=2. In that case use slprints=2.01
exlumpr	Real	In log10	Proton injection compactness (dimensionless measure of proton injection luminosity)
bpresc	Real	1. (default)	Proton escape rate in units of the light crossing time
ap	Real	>=0	Exponent index of exponential cutoff in proton PL energy spectrum
ipexp	Integer	0/1	Flag for proton PL (or BPL) without/with exponential cutoff
ielext	Integer	0/1	Flag for switching off/on external injection of electrons with power law (PL) energy spectrum
geextmn	Real	In log10	Min value of electron PL or BPL
geextmx	Real	In log10	Max value of electron PL or BPL
slelints	Real		Slope of electron PL. NOTE – the code crashes if slerints=2. In that case use slerints=2.01
exlumel	Real	In log10	Electron injection compactness (dimensionless measure of electron injection luminosity)
belesc	Real	1. (default)	electron escape rate in units of the light crossing time
ae	Real	>=0	Exponent index of exponential cutoff in electron PL energy spectrum
ieexp	Integer	0/1	Flag for electron PL (or BPL) without/with exponential cutoff
iphotext	Integer	0/1	Flag for switching off/on external fixed photon field with grey body energy spectrum
temperat	Real	[Kelvin]	Temperature of grey body
exlumth	Real		Compactness of grey body field (dimensionless measure of photon energy density)
iphotext2	Integer	0/1	Flag for switching off/on external fixed photon field with broken power-law (BPL) energy spectrum
x1	Real	[in me c2 units]	Min. energy of BPL
x2	Real	[in me c2 units]	Max. energy of BPL
xbr	Real	[in me c2 units]	Break energy of BPL. NOTE – if xbr=x2, then one models a simple PL
beta1	Real		Power-slope before the break energy of the BPL
beta2	Real		Power-slope after the break energy of the BPL
extph0	Real		Compactness of BPL photon field (dimensionless measure of photon energy density)
ielextbr	Integer	0/1	Flag for external injection of electrons without/with broken power law (BPL) energy spectrum
geextbr	Real	In log10	Electron break Lorentz factor
slelints1	Real		Power-slope before the break energy of the electron BPL
slelints2	Real		Power-slope after the break energy of the electron BPL
ae2	Real	>=0	Exponent index of exponential cutoff in electron BPL energy spectrum
iprextbr	Integer	0/1	Flag for external injection of protons without/with broken power law (BPL) energy spectrum
gpextbr	Real	In log10	Proton break Lorentz factor
slprints1	Real		Power-slope before the break energy of the proton BPL
slprints2	Real		Power-slope after the break energy of the proton BPL
ap2	Real	>=0	Exponent index of exponential cutoff in proton BPL energy spectrum
isyn	Integer	0/1	Flag for switching off/on electron synchrotron
iprsyn	Integer	0/1	Flag for switching off/on proton synchrotron
issa	Integer	0/1	Flag for switching off/on synchrotron self-absorption
icompt	Integer	0/1	Flag for switching off/on inverse Compton scattering
ikn	Integer	0/1	Flag for switching off/on computation of electron losses in the Klein-Nishina regime using the full expression from Bloumenthal & Gould (1970)
igg	Integer	0/1	Flag for switching off/on photon-photon pair production
ianni	Integer	0/1	Flag for switching off/on electron-positron annihilation
iesc	Integer	0/1	Flag for switching off/on electron and proton escape
ipsc	Integer	0/1	Flag for switching off/on photon, neutrino, and neutron escape

Code normalization
All number densities in the code are dimensionless (normalized to σΤ*radius)
Time is also dimensionless (normalized to radius/c)
For details, see Refs. 1+2 below

List of main output files

– fort.81 → contains snapshots of photon spectra (including any potential external photon field): log10(x), log10(x2 nγ(x,t))
– fort.71 → contains snapshots of photon spectra (excluding any potential external photon field): log10(x), log10(x2 nγ(x,t)), log10(x2 nγ, ext (x))
– fort.89 → contains snapshots of electron/positron spectra: log10(γ), log10(γ2 ne(γ,t))
– fort.88 → contains snapshots of proton spectra: log10(γ), log10(γ2 np(γ,t))
– fort.72 → dimensionless bolometric light curve time: time, log10(nph), where nph = \int nγ(x,t) dx
## Questions and Problems
TBD

Publications with the code description:
1. Mastichiadis & Kirk, A&A (1995): description of the time-dependent lepto-hadronic code with acceleration. Simplified expressions for photohadronic losses and production of secondaries; linear acceleration term.
2. Mastichiadis, Protheroe & Kirk, A&A (2005): improved description of Bethe-Heitler interactions using Monte Carlo results from Protheroe & Johnson (1996)
3. Dimitrakoudis, Mastichiadis, Protheroe & Reimer, A&A (2012): improved description of photopion interactions using SOPHIA Monte Carlo results.